## Slide 1: Motors and Generators

## Slide 2: Lorentz Force (Motor Equation)
Wire page in uniform B
Exerts a downward force
Adds up
subtracts
Lorentz’s

## Slide 3
In a motor, two conductors (of coil) are mounted on a rotor with axis. The rotor experiences a total turning torque
1
1
Relationship between force F, torque τ, linear momentum p, and angular momentum L in a system which has rotation constrained to only one plane (https://en.wikipedia.org/wiki/Torque)
Rotor Experiencing a Torque

## Slide 4: Motor and Generator Equations
Motor equation
Generator equation

## Slide 5
Induced EMF on moving conductor
Generator equation
A conductor moving to right with velocity v across a uniform magnetic field B generates an EMF over infinitesimal length dL as
Thus, a moving conductor through a magnetic flux density B with velocity v produces an electric field E along the conductor. Integrating E over the length L gives the total induced EMF
Max

## Slide 6
Example: Generator voltage: Given that L = 0.4m, velocity = 3 m/s, and B = 2 milliTesla, and
Solution:
Max
Solution:

## Slide 7: Torque on a current loop in a Magnetic Field
Torque is clockwise as viewed from top side
Uniform Magnetic flux density B across North and south poles
Current carrying coil having uniform current I and area A= lw

## Slide 8
Loop at different rotation angels as viewed from top
general
Max torque
0 torque
Negative torque

## Slide 9
Torque is clockwise as viewed from top side
Perpendicular to the loop makes an angle with the field that is the same as angle between lever w/2 and F
F
Forces on the top and bottom segments are vertical and, therefore, parallel to the shaft, producing no torque
For N turns:
Each vertical segment has a length L that is perpendicular to B

## Slide 10
Find the maximum torque on a 100-turn square loop of a wire of 10.0 cm on a side that carries 15.0 A of current in a 2.00-T field.
Solution:
Torque on the loop can be found using
Maximum torque occurs when θ = 90º and sin θ = 1.
For sin θ = 1, the maximum torque is
Entering known values yields
τmax= (100)(15.0 A)(0.100 m2)(2.00 T) = 30.0 N⋅m
Sufficient to be used in motors.

## Slide 11
The torque found in the preceding example is the maximum. As the coil rotates, the torque decreases to zero at θ=0. The torque then reverses its direction once the coil rotates past θ=0. This means that, unless we do something, the coil will oscillate back and forth about equilibrium at θ=0
As the angular momentum of the coil carries it through the zero-torque point, the brushes reverse the current direction to keep the torque clockwise. In the right figure coil will rotate continuously in the clockwise direction reversing every half-cycle to maintain clockwise torque