## Slide 1: Waveguides

## Slide 2: Waveguides
Rectangular waveguide
Waveguide to coax adapter
A waveguide is a structure that guides waves with minimal loss of energy by restricting the transmission of energy to one direction.
Rectangular waveguides are one of the earliest type of the transmission lines. They are used in many applications. A lot of components such as isolators, detectors, attenuators, couplers and slotted lines are available for various standard waveguide bands between 1 GHz to above 220 GHz.
Parallel Plate Waveguides

## Slide 3
Waveguides
In electromagnetic wave propagation, the propagation is via the transverse electromagnetic (TEM) mode, meaning both the electric and magnetic field components were transverse, or perpendicular, to the direction of propagation.
Here, we investigate wave-guiding structures that support propagation in non-TEM modes, namely in the transverse electric (TE) and transverse magnetic (TM) modes.
In general, the term waveguide refers to constructs that only support non-TEM mode propagation. Such constructs share an important trait: they are unable to support wave propagation below a certain frequency, termed the cutoff frequency.
In that sense parallel plate waveguides are exception as they do allow propagation of TEM modes.
Optical Fiber
Dielectric Waveguide
Rectangular Metallic Waveguide
Circular Metallic Waveguide

## Slide 4
Wave Propagation along Uniform Guiding structures:
Assuming wave propagate in + z direction
Uniform Waveguide with arbitrary section
E0(x , y) is two-dimensional vector phasor that depends only on cross-sectional coordinates
When working with phasors we can drop the time and z-dependence as shown in exponential variation. We can simply replace partial differentials with z and t by multiplying with -𝛾 and
Cross-section
Propagation along z
Conductor
Dielectric filled or hollow
We can write H (x, y, z, t) in a similar manner

## Slide 5
Uniform Waveguide with arbitrary section
Consider a straight waveguide in form of a dielectric filled metal tube having an arbitrary cross-section
For charge free region:
We can write the homogenous vector Helmholtz’s equations as follows:
Where E and H are 3-dimensional vector phasors, k is the wave number
Expanding in rectangular coordinates, and using while removing time dependence, we have

## Slide 6
Recalling Maxwell’s Equation, we have
Expanding curls and separating, we get

## Slide 7
Putting the value of Ey0 from second expression on the Right side into first equation, we get
We have derived expressions for one component of H in terms of Hz and Ez
But why, So that we can define wave propagation mode using Hz and Ez, and their characteristics

## Slide 8
It is convenient to classify the propagating waves in a uniform waveguide into three types according to whether Hz and/or Ez exists.
Transverse Electromagnetic (TEM) Waves. These are waves that contain neither Hz nor Ez.
2. Transverse Magnetic (TM) Waves. These are waves that contain a nonzero Ez but Hz =0.
3. Transverse Electric (TE) Waves. These are waves that contain a nonzero Hz but Ez= 0.
The propagation characteristics of the various types of waves are different; they will be discussed in subsequent subsections.

## Slide 9
For TEM Wave: Hz and Ez will be zero, therefore all the above equations constitute a set of trivial solutions (all field components vanish).
unless the denominator h2 also equals zero ().
Similarly, we can get, other components in terms of Hz and Ez
Same as plane wave in unbounded medium

## Slide 10
Propagation Velocity
Wave Impedance
General form for (E/H) Impedance relation
Hz

## Slide 11
Parallel Plate Waveguide:
Allows for TEM wave propagation.
Also supports TE/TM wave propagation
For TM mode: Hz = 0
Boundary Condition
Propagation along z
Parallel Plate Waveguide:
Tangential E must vanish
Conductor

## Slide 12
At cutoff frequency  = 0
For TM mode: Hz = 0
An is the magnitude of excitation

## Slide 13
The lowest frequency mode allowed is called dominant mode: Here it is TEM mode.
At cutoff frequency  = 0

## Slide 14
Filed lines for TM1 Mode in parallel plate waveguide:
E = Ez
Ez max at y = b/2
Ez
|Ey|max at y = b
|Ey|max at y = 0
At y = 0 and b, there will be surface currents due to discontinuity in the tangential H field whereas there will be surface charges due presence of normal electric field (in accordance with boundary conditions around conductors)

## Slide 15
TE Waves between Parallel Plates
Boundary Condition
Ez = 0
Parallel Plate Waveguide:
Ex must vanish
Notice the differential
Propagation along z
Conductor

## Slide 16
The cutoff frequency for TEn and TMn mode for a parallel plate waveguide is same.
For n = 0, both Hy and Ex vanish; hence the TE0 mode does not exist in parallel plate waveguide

## Slide 17
Filed lines for TE1 Mode in parallel plate waveguide:
Hz max at y = b
|Ex| max at y = b/2
Hz = 0
Hz max at y = 0
Propagation along z
y
z
At y = 0 and b, there will be surface currents due to discontinuity in the tangential H field whereas there will be surface charges due presence of normal electric field (in accordance with boundary conditions around conductors)

## Slide 18: Rectangular waveguide Analysis

## Slide 19
The analysis of parallel-plate waveguides in previous slides we assumed the plates to be of an infinite extent in the transverse x direction; that is, the fields do not vary with x.
In practice, these plates are always finite in width, with fringing fields at the edges. Electromagnetic energy will leak through the sides of the guide and create undesirable stray couplings to other circuits and systems.
Thus, practical waveguides are usually uniform structures of a cross section of the enclosed variety. The simplest of such cross sections, in terms of ease both in analysis and in manufacture, are rectangular cross-and circular sections.
We will deal with rectangular waveguide as it is easier to analyse. Circular geometry requires knowledge of Bessel’s functions and hence will be skipped in the course.
TEM waves are not supported in cross-section of enclosed variety.
Rectangular waveguides:

## Slide 20: TEM mode does not exist in rectangular waveguides….
Assume, TEM exists inside a rectangular waveguide, the lines of B or H will be closed loops in the plane perpendicular to the direction of propagation. According to Maxwell’s first equation the magnetomotive force (MMF) around each of this closed loop must be equal to the current (conduction or displacement) passing through the loop.
In the case of guide with an inner conductor, like a coaxial cable, the current through the H loops is the conduction current in the inner conductor.
However, for a hollow wave guide having no inner conductor, this axial current must be a displacement current. But axial displacement current requires an axial component of D or E, which is not present in a TEM wave
So, TEM wave or mode cannot exist in a single-conductor waveguide.

## Slide 21
A waveguide will propagate “higher-order” modes, which are classified as either transverse magnetic (TM) or transverse electric (TE).
There are two problems with propagating higher-order modes:
TE and TM modes have a limited bandwidth. In fact, none of these modes can propagate at frequencies below a minimum frequency known as the cutoff frequency.
2. TE and TM modes are dispersive. That is, the phase velocity is dependent on frequency—for some modes highly dependent!
A waveguide also has two important advantages.
1. It can typically handle very large power (e.g., kilowatts).
2. It can have very low loss (low value of α).

## Slide 22
Transverse Magnetic Waves in rectangular waveguides:
For transverse magnetic (TM) waves: Hz = 0
While we have written Ez as phasor
Propagation along z
b
x
z
Conducting walls
a
y
a > b
Second order PDE

## Slide 23
Assuming Ez as product of two separate functions in x and y, we write
Substitution in PDE and dividing by Ez gives:
Rearranging, we have

## Slide 24
Along the x-direction, boundary conditions
Propagation along z
b
x
z
Conducting walls
a
y
Tangential E must vanish
Applying boundary conditions we get

## Slide 25
For TM Wave Hz = 0
b
x
z
a
y
Since we have the expression for Ez, we can use
z = 0 plane

## Slide 26
m and n define a possible mode that may be designated as TMmn mode.
m: The number of half cycle variations in x-direction
n: The number of half cycle variations in y-direction
For TM modes in rectangular waveguides, neither m nor n can be zero
The lowest mode/ dominant mode will be TM11 mode
The mode having lowest cutoff frequency is called the dominant frequency

## Slide 27
TM11 Mode Pattern
y
z
y
x
y
E and H line are perpendicular to one another everywhere
E lines are normal while H lines are parallel to conductor walls

## Slide 28
At cutoff  = 0
Cutoff Frequency for various modes:

## Slide 29
i
Allows guided propagation
Above cutoff
where
Guided wavelength
Where,

## Slide 30
Phase Velocity:
Group Velocity:
In Waveguide
Waveguide is called dispersive because phase velocity is function of frequency
Propagation constant

## Slide 31
Wave Impedance:
Propagation factor becomes
The wave diminishes rapidly with z and is said to be evanescent.
Waveguide behaves as high pass filter.

## Slide 32
Transverse Electric Waves:
For transverse magnetic (TM) waves: Ez = 0
While we can write Hz as phasor
Propagation along z
b
x
z
Conducting walls
a
y

## Slide 33
Boundary Conditions:
In x-direction
In y-direction
b
x
z
a
y

## Slide 34
b
x
z
a
y
On solving using procedure as TM case:

## Slide 35
For TE modes, either m or n (but not both) can be zero.
If a>b the lowest mode will be TE10 mode
m: The number of half cycle variations in x-direction
n: The number of half cycle variations in y-direction

## Slide 36
Phase Velocity:
Group Velocity:
Wave Impedance:
Allows guided propagation

## Slide 37: Uniform Plane waves
Constant phase planes moving the distance

## Slide 38: Uniform Plane waves
At successive times curve effectively travels in + x
A point of constant phase moves forward.
= constant
Phase velocity: velocity of Equi phase front

## Slide 40
Wave Propagation inside the waveguide
The Phase velocity is given by
using
The Group velocity is given by
The Wave velocity is given by
Wave velocity
Phase velocity
Group velocity
Beach
Ocean
Phase velocity
Wave velocity
Group velocity
Analogy!
Point of contact

## Slide 41
- diagram for waveguide
For TEM: Constant slope;
Same as velocity of light in an unbounded dielectric medium with constitutive parameters  and 
For TE or TM: slope is not constant
It intersects the  axis (=0) at  = c
OP slope represents the phase velocity at that point P.
Local slope represents the group velocity at point P.

## Slide 42
Example
Rectangular Waveguide
Let’s determine the TE mode impedance looking into a 20 cm long section of shorted WR90 waveguide operating at 10 GHz.
From the Waveguide Table 7.1, a = 0.9 inch (or) 2.286 cm and b = 0.450 inch (or) 1.143 cm.
TE10
6.56 GHz
Mode
Cutoff Frequency
TE01
13.12 GHz
TE11
14.67 GHz
TE20
13.13 GHz
TE02
26.25 GHz
At 10 GHz, only the TE10 mode is supported!
TE10
6.56 GHz
Mode
Cutoff Frequency
TE01
13.12 GHz
TE11
14.67 GHz
TE20
13.13 GHz
TE02
26.25 GHz
TE10
TE20
TE01
TE11
TM11
6.56 GHz
13.12 GHz
TE02
26.25 GHz
14.67 GHz
Rearrange
13.13 GHz

## Slide 43
Example
Rectangular Waveguide
The TE10 mode impedance
The TE10 mode propagation constant is:
The impedance looking into a short circuit is given by

## Slide 44
Example: Determine (a) the wave impedance and guided wavelength at a frequency equal to twice the cutoff frequency in a waveguide for TEM, TE and TM modes.
(b) Repeat the same calculations when the operating frequency is half the cutoff frequency.
Case 1: = 1/4
TEM

## Slide 45
(b) Repeat the same calculations when the operating frequency is half the cutoff frequency.
Case 2: = 4; evanescent wave
TEM

## Slide 46: Propagation inside a Waveguide
Port1
Port2
TE10 mode propagation in a rectangular Waveguide

## Slide 47
Surface Currents on guide wall for TE10 mode